## Slide 1
HPGe MCNP Automated Parametric Optimization Model
Air Force Institute of Technology
6 December, 2017

## Slide 2: Overview
Project Goal
Previous Work
Experiment
MCNP Model
Parametric Optimization Code
Results
Future Work

## Slide 3: Project Goal
Build a model of a High-Purity Germanium (HPGe) Detector using MCNP
Create a parametric automated optimization code to match experimental and simulated efficiencies
Perform an adjoint flux calculation using ADVANTG

## Slide 4: Previous Work
Manufacturer provided dimensions are often times not sufficient for developing models. [1]
Published relative differences between experimental and Monte Carlo simulated absolute efficiencies range from around 10% to as low as 0.2%. [2][3]
Dead layer thickness and the active volume may change over time. [4]
Notes: [1] Ronald Keyser
[2] https://cyclotron.tamu.edu/progress-reports/2002-2003/1%20Nuclear%20Structure,%20Fundamental%20Interactions,%20and%20Astrophysics/I-28%20Precise%20efficiency%20calibration%20of%20an%20HPGe%20detector.pdf
[3]http://www.iaea.org/inis/collection/NCLCollectionStore/_Public/42/107/42107607.pdf
[4] Knoll’s

## Slide 5: Experiment
Performed by Lt Col O’Day (April 2017)
Eckert & Ziegler Multi-nuclide source
24-hour measurements
5 different source positions
Notes: [1] Ronald Keyser
[2] https://cyclotron.tamu.edu/progress-reports/2002-2003/1%20Nuclear%20Structure,%20Fundamental%20Interactions,%20and%20Astrophysics/I-28%20Precise%20efficiency%20calibration%20of%20an%20HPGe%20detector.pdf
[3]http://www.iaea.org/inis/collection/NCLCollectionStore/_Public/42/107/42107607.pdf
[4] Knoll’s

## Slide 6: Detector Specifications
Canberra Standard Electrode Ge Detector (SEGe)
Model Number: GC10021
Relative Efficiency 100 %
Resolution: 1.20 keV at 122 keV and 2.1 at 1.3 MeV
Coaxial Configuration
P-Type
n+ contact
p+ contact
e-
γ
Notes: [1] Ronald Keyser
[2] https://cyclotron.tamu.edu/progress-reports/2002-2003/1%20Nuclear%20Structure,%20Fundamental%20Interactions,%20and%20Astrophysics/I-28%20Precise%20efficiency%20calibration%20of%20an%20HPGe%20detector.pdf
[3]http://www.iaea.org/inis/collection/NCLCollectionStore/_Public/42/107/42107607.pdf
[4] Knoll’s

## Slide 7: Detector Specifications
Notes: [1] Ronald Keyser
[2] https://cyclotron.tamu.edu/progress-reports/2002-2003/1%20Nuclear%20Structure,%20Fundamental%20Interactions,%20and%20Astrophysics/I-28%20Precise%20efficiency%20calibration%20of%20an%20HPGe%20detector.pdf
[3]http://www.iaea.org/inis/collection/NCLCollectionStore/_Public/42/107/42107607.pdf
[4] Knoll’s

## Slide 8: Experimental Setup
Notes: [1] Ronald Keyser
[2] https://cyclotron.tamu.edu/progress-reports/2002-2003/1%20Nuclear%20Structure,%20Fundamental%20Interactions,%20and%20Astrophysics/I-28%20Precise%20efficiency%20calibration%20of%20an%20HPGe%20detector.pdf
[3]http://www.iaea.org/inis/collection/NCLCollectionStore/_Public/42/107/42107607.pdf
[4] Knoll’s

## Slide 9: Experimental Setup
Gamma-Ray Energy [keV] | Nuclide | Activity [µCi] | Gammas per Second
60 | Am-241 | 0.02941 | 391.7
88 | Cd-109 | 0.2707 | 363.6
122 | Co-157 | 0.01019 | 322.7
159 | Te-123 | 0.01403 | 436.1
320 | Cr-51 | 0.3389 | 1236
392 | Sn-113 | 0.05109 | 1227
514 | Sr-85 | 0.06171 | 2247
662 | Cs-137 | 0.04325 | 1362
898 | Y-88 | 0.09633 | 3347
1173 | Co-60 | 0.05101 | 1885
1333 | Co-60 | 0.05101 | 1887
1836 | Y-88 | 0.09622 | 3539
* Energies were kept constant with manufacturer provided documentation
* Source uncertainty for each energy was 3.1%
Notes: [1] Ronald Keyser
[2] https://cyclotron.tamu.edu/progress-reports/2002-2003/1%20Nuclear%20Structure,%20Fundamental%20Interactions,%20and%20Astrophysics/I-28%20Precise%20efficiency%20calibration%20of%20an%20HPGe%20detector.pdf
[3]http://www.iaea.org/inis/collection/NCLCollectionStore/_Public/42/107/42107607.pdf
[4] Knoll’s

## Slide 10: Experimental Setup
(0,0)
X-axis
y-axis
A
B
C
D
E
F
G
A – 13.7385 cm
B – 3.48 cm
C – 4.8885 cm
D – 7.6 cm
E – 20.735 cm
F – 29.7385 cm
G – 9.78 cm
1
2
3
4
5
Notes: [1] Ronald Keyser
[2] https://cyclotron.tamu.edu/progress-reports/2002-2003/1%20Nuclear%20Structure,%20Fundamental%20Interactions,%20and%20Astrophysics/I-28%20Precise%20efficiency%20calibration%20of%20an%20HPGe%20detector.pdf
[3]http://www.iaea.org/inis/collection/NCLCollectionStore/_Public/42/107/42107607.pdf
[4] Knoll’s

## Slide 11: MCNP Model

## Slide 12: Geometry
Origin: Centered/Bottom of shielding case
Cylinders (~14 CZs)
Planes (~20 PZs)

## Slide 13: Geometry
Top View:

## Slide 14: Materials
Material | Density [g/cm3] | Component(s)
Mylar | 1.38 | IR Window
Brass | 8.41 | Metal Clasps
Aluminum | 2.7 | Detector Housing and Casing
Germanium | 5.32 | Ge Crystal
Lithium | 0.534 | Outer Deadlayer
Boron | 2.73 | Inner Deadlayer
Copper | 8.96 | Shield Lining
Tin | 7.31 | Shield Lining
Kapton Film | 1.42 | IR Window
Air | 0.001224 | Shielding Chamber
Lead | 11.34 | Shielding
Acrylic Glass | 1.19 | Source Encapsulation
Vacuum | --- | Coaxial Space
* All materials from LANLs ACE Data Tables, or PNNLs Compendium of Material Composition Data for Radiation Transport Modeling

## Slide 15: Photon Transport
Only photons
5 MeV upper limit
No Bremsstrahlung
No Coherent scattering
No photofission
Doppler broadening on
No photofission
Notes: Cite manual, primer, and PNNL materials

## Slide 16: Source Definition
Isotropic point source
11 discrete energies
106 source particles
Gaussian broadening off
Tallies:
  F8 – Energy Deposition Tally
    Ge Crystal (Cell 3)
    8192 bins (10-5 - 3.14344 MeV)

## Slide 17: Paremeters to Adjust
Isotropic point source
11 discrete energies
106 source particles
Gaussian broadening off
Tallies:
  F8 – Energy Deposition Tally
    Ge Crystal (Cell 3)
    8192 bins (10-5 - 3.14344 MeV)

## Slide 18: Summary
Background
MCNP Model
Parametric Optimization Code
Results
Future Work

## Slide 19: Acknowledgements
Captain James Bevins, AFIT
Lt Colonel Buck O’Day, AFIT
Edna’s Model
Capt Bevins Model

## Slide 20: References
[1] Ronald Keyser
[2] https://cyclotron.tamu.edu/progress-reports/2002-2003/1%20Nuclear%20Structure,%20Fundamental%20Interactions,%20and%20Astrophysics/I-28%20Precise%20efficiency%20calibration%20of%20an%20HPGe%20detector.pdf
[3]http://www.iaea.org/inis/collection/NCLCollectionStore/_Public/42/107/42107607.pdf
[4] Knoll’s
[5] Standard Electrode Coaxial Ge Detectors

## Slide 21: Questions?